THERMAL ANALYSIS OF RF SECTION OF 250kW

C-BAND KLYSTRON

Suman Baloda, O S Lamba, Richa Badola, Meenu Kaushik, Pradeep, Deependra Kant , L M Joshi,

Microwave Tubes Area

CSIR – Central Electronics Engineering Research Institute,

Pilani (Rajasthan):333031

osl@ceeri.ernet.in

Abstract: The paper presents the design and development of RF section   for C-band 250 kW high power klystron. Klystron is vacuum electron device operating in microwave range of frequencies. It is used as power amplifier in a variety of systems including radars, particle accelerators and thermonuclear reactors. The paper deals with thermal analysis of RF-section of a 250KW CW C-band Klystron. Before doing thermal analysis of RF section using ANSYS, the model constructed with the help of Poisson’s Superfish, AJ-Disk and Magic 2D soft-wares is simulated to observe the electron-beam interaction in the RF-section of the Klystron. The results of these simulations i.e. R/Q, Q and the voltage across the gap of the cavity are then used to calculate heat dissipated in the RF section. The input parameters used in thermal simulation are heat flux, heat transfer coefficient and output parameter is thermal temperature.

Keywords- RF section; Beam wave interaction; klystron;

I	INTRODUCTION

This klystron consists of an input cavity, four buncher cavities, and an output cavity. The RF signal to be amplified at the input cavity starts the velocity modulation process. Klystron is a velocity-modulated tube in which the velocity modulation process produces a density-modulated beam of electrons. The RF signal is carried from cavity to cavity by the electron beam. This klystron consists of an input cavity, four buncher cavities, and an output cavity.

The RF signal to be amplified at the input cavity starts the velocity modulation process. The field free space between cavities allows the beam to drift and form bunches. Each subsequent cavity couples to the beam, reinforcing bunching energy.

The output cavity couples energy from the beam to the output waveguide.

The thermal simulation has been done using ANSYS 11.0 (multi-physics). RF section has designed for 1 kW power dissipation. The input parameters used in thermal simulation are heat flux, heat transfer coefficient and output parameter is thermal temperature. OFHC copper material is chosen for RF section which is suitable for vacuum and hydrogen brazing operations and good thermal properties for efficient cooling.

Specifications of this particular klystron

Operating Frequency: 		5 GHz

Output Power:			250 kW CW

Beam Voltage:			60 kV

Beam Current:			10 Amp

Focusing:			Electromagnet

No. of cavities: 			6

Efficiency:			40 % (min.)

Gain:				45 dB (min.)

Cooling:				Water

II	DIMENSION OF RF SECTION

No. of cavities			6

OD of cavity			26.55 mm

ID of cavity			32.55 mm

Cavity height 			15 mm

OD of drift tube			16.5 mm

ID of drift tube			8.5 mm

RF section Length		360 mm

Total Surface Area		231.905 cm2

Power Dissipation		1 kW

III	THERMAL ANALYSIS OF RF 	SECTION

The thermal analysis has been done using ANSYS 11.0 (multi-physics). A thermal analysis calculates the temperature distribution and related thermal quantities in a system or component. The basis for thermal analysis in ANSYS is a heat balance equation obtained from the principle of conservation of energy. The input parameters used in thermal simulation are heat flux, heat transfer coefficient and output parameter is thermal temperature of RF section. A forced water cooled RF section has been designed to dissipate 1kW power. The temperature analysis is carried out for RF section. The temperature rise of the surface calculated for 5 l/min. to 10 l/min. flow rate. The temperature rise of the surface calculated for 5 l/min. flow rate. The desired flow rate is optimized for safe limit of temperature rise of RF section. The desired flow rate is optimized for safe limit of temperature rise of RF section. RF section has designed for 1 kW power dissipation. The output voltage obtained by AJDISK and power dissipation is calculated by this formula-

=

Using above formula we have calculated power dissipation individually for each cavity. Calculated power dissipation for first cavity is 0.106 W, for second cavity is 2.35W, for third cavity is 4.14W, for fourth cavity is 41.21W, for fifth cavity is 215 W and for sixth cavity is 689.30W. Total power dissipation for RF section is calculated 952.11W.

Heat transfer occurs between a moving fluid and solid surface. The rate of heat transfer between a surface and a fluid is given by:

h =  {Kw  / DH }.Nu

where Kw is Thermal  Conductivity(Wm-1K-1), DH is Hydraulic diameter(m) and Nu is  Nusselt number.

Output cavity design:

The output voltage of output  cavity is shown in figure1 taken from MAGIC 2D code is obtained 53.4kV. Using above formula we have calculated power dissipation for output cavity is 689.30 W. and calculated heat flux and film coefficient of output cavity are 29725.10 w/m2 and 13518.51w/m2K respectively. These Obtained values are used as input of thermal analysis of sixth cavity. Thermal analysis of output  cavity has been done using ANSYS code and we have got the surface temperature of the output cavity to be 38.02-45.020C. Temperature profile shown in figure2.

Fig 1: output cavity voltage

Fig 2: Temperature  profile of  output cavity

Fig 3: Output power delivered at load

Fig 4: Beam energy Vs axial distance

Calculated heat flux and film coefficient of RF section are 41056.16 w/m2 and 13518.51w/m2K respectively. Then heat flux and heat transfer so obtained are used as input for thermal analysis of RF section. For different condition of the flow different values of heat transfer coefficient are obtained and are given as input to the ANSYS and temperature distributed on geometry surface is obtained as shown in Table1 and temperature profile shown in figure6.

Fig 5: Mesh geometry of RF section

Fig 6: Temperature  profile of  RF section

Table 1 Simulated temperatures with varying flow rates:

| Water Flow(lpm) | Applied heat flux (w/m2) | Cooling coefficient (w/m2K) | Simulated temp.(0C) in ANSYS |
| --- | --- | --- | --- |
| 5 | 41056.16 | 3518.51 | 37.32-48.29 |
| 10 | 41056.16 | 6126.10 | 33.65-39.25 |

FABRICATED ASSEMBLY OF RF SECTION PARTS

IV	CONCLUSION

The thermal design of RF section assembly with cooling system for 250 kW C band klystron has been done successfully. Thermal analysis of RF section has been done using ANSYS code and we have got the surface temperature of the RF section to be 37.32-48.290C which is quite easy to maintain. The fabrication of RF section is under progress.

ACKNOWLEDGEMENT

The authors are thankful to Dr. Chandra Shekhar, Director CEERI and Dr SN Joshi, project advisor, Microwave Tube Area for permission to present this work and their encouragement.

REFERENCES

[1] Allan W. Scott, “Cooling of Electronic Equipments”, John Willey and sons.

[2] Frank P Incropera, “Introduction to Heat Transfer”, John Willey and sons.

[3]  ANSYS  user manual, supplied with software.

[4] Robert M. Philips and Daryl W. Sprelin, High power klystrons for next linear colliders, Proceeding of IEEE, Vol 87, No.5, May 1999.

[5]  MAGIC user help manual.

[6]  AJDISK help Manual.