Design and Development of  RF section  for   250 kW CW

C-band Klystron

O S Lamba , Richa Badola, Meenu Kaushik,  Pradeep, Suman Baloda, Vrati, Kirti,  L. M. Joshi

Microwave Tubes Area.

CSIR-Central Electronics Engineering Research Institute, Pilani

(Rajasthan):333031

osl@ceeri.ernet.in

Abstract

Klystron is a microwave tube capable to produce very high power that find wide use in communication, radar, material processing, particle accelerator and thermonuclear fusion reactor. A precise simulation of beam wave interaction in klystron is useful not only to understand its operation but also in development of tube with minimum iterations in fabrication. For this purpose a 1-D code AJDISK has been used to estimate different design parameters of RF section for desired tube performance. This information is used for simulation of complete tube including electron gun using MAGIC 2D PIC code. The paper presents the results of simulation.

Keywords—Klystron, cavity, beam voltage, axial distance

I. Introduction

This klystron consists of an input cavity, four buncher cavities, and an output cavity. The RF signal to be amplified at the input cavity starts the velocity modulation process. The field free space between cavities allows the beam to drift and form bunches. Each subsequent cavity couples to the beam, reinforcing bunching energy. The output cavity couples energy from the beam to the output waveguide. Cavities 1, 2, and 3 are stagger-tuned to achieve required flat bandpass response. Cavities 4 and 5 are tuned for efficiency at a frequency above the highband edge, enhancing bunching action of the beam. Cavity 6, the output cavity, is always tuned to center frequency.

A 250 kW CW C-Band klystron with specifications as given in Table1 is under development at CEERI, Pilani (India)

Table1: Specifications of 5GHz klystron

| Parameters | Specification |
| --- | --- |
| Operating frequency | 5 GHz |
| Output power | 250 kW |
| Beam voltage | 50 kV |
| Beam current | 10 A |
| No. of cavities | 6 |
| Efficiency | >40% |
| Gain | >40dB |

II.  Design of RF cavities using Poisson's Superfish

Poisson’s Superfish is a collection of programs for calculating static magnetic and electric fields and radio-frequency electromagnetic fields in either 2-D Cartesian coordinates or axially symmetric cylindrical coordinates. The programs generate a triangular mesh fitted to the boundaries of different materials in the problem geometry.

Plotting programs and other postprocessor codes present    the results in various forms. We design individual Cavities   and calculate their respective R/Q in Poisson’s Superfish.

Design of input and intermediate cavities:

Input parameters

Height of cavity- 15mm

Radius of cavity- 13.75mm

Height of drift tube- 5.75mm

Radius of drift tube- 4mm

Figure1: Graphical representation of Input Cavity using   Poisson’s Superfish

Output parameters

Frequency-5008 MHz

R/Q-105

K-250

Design of output cavity:

Input parameters

Height of cavity- 15mm

Radius of cavity- 13.48mm

Height of drift tube- 6mm

Radius of drift tube- 4mm

Figure2: Graphical representation of Output Cavity using Poisson’s       Superfish

Output parameters

Frequency-5002 MHz

R/Q-103

K-260

III. Design of RF section using 1-D code AJDISK

AJDISK is a 1-D large signal code developed by A.Jensen and is available in public domain. It is an ideal code for quickly estimating the basic design of klystron. Input needed to run the program include resonant frequency, Qs, R/Q and gap voltage of each cavity, axial distance between the gap centres, operating beam voltage, current and drive power. The output of the program includes gain, output power, cavity voltages, phase diagram and velocity dispersion diagram. A typical output generated by the Program for design of present tube is shown in figure3 and figure 4.

At 50kv beam voltage: When 50kv beam voltage and 10Amp current is applied at the input of RF section the Output Power obtained is 242KW.

figure3: Graphical representation of beam wave   interaction simulation using AJDISK at 50kv beam voltage

At 52kv beam voltage: When 52kv beam voltage and 10Amp current is applied at the input of RF section the Output Power obtained is 251KW.

###### Figure4: Graphical representation of beam wave   interaction simulation using AJDISK at 52kv beam voltage

###### Table 2 : Input parameters for RF section of length 340 mm

| CAVITY | Z (Distance in mm) | Frequency in MHz | R/Q | Qe |
| --- | --- | --- | --- | --- |
| Cavity 1 | 0 | 5000 | 105 | 300 |
| Cavity 2 | 53 | 4984 | 105 | 4000 |
| Cavity 3 | 106 | 5087 | 105 | 4000 |
| Cavity 4 | 205 | 5140 | 105 | 4000 |
| Cavity 5 | 277 | 5098 | 105 | 4000 |
| Cavity 6 | 319 | 5000 | 103 | 70 |

IV. Simulation of cavity using MAGIC 2D PIC code

MAGIC is particle-in-cell code developed by Mission Research Corporation, USA. The code is available both in 2D and 3D versions. It simulates actual electric and magnetic fields by tracing the outlines of RF cavities, drift tubes and pole pieces on closely spaced grids pushing thousands if simulated electrons through these simulated fields and iterating to convergence. The code is capable of designing electron gun and cavity as well. Following figures show the result of cavity simulation using MAGIC code.

figure5: simulation of input cavity using magic 2D

figure6:frequency of input cavity using magic 2D

figure7:R/Q of input cavity using magic 2D

Fabrication and cold testing of input and output cavity

Fabricated Input Cavity

figure8:fabricated input cavity

figure9: testing of input cavity

| Parameters | Analytical Input Section | Simulated value CST |
| --- | --- | --- |
| Frequency | 5.0GHz | 5.0005GHz |
| Return-loss | 1.43 dB | 1.433dB |
| Band-width | 16.67MHz | 16 MHz |

Fabricated Output Cavity:

figure10:fabricated output cavity

figure11: testing of output cavity

| Parameters | Analytical Input Section | Simulated value CST |
| --- | --- | --- |
| Frequency | 5.0GHz | 5.0005GHz |
| Return-loss | 0.33 dB | 0.457dB |
| Band-width | 69.50MHz | 60 MHz |

V. validation of RF section design using MAGIC CODE

Result at 53KV beam voltage: At 53KV beam voltage output   power obtained is 230KW in magic software

figure12: simulation of RF section and beam wave interaction

figure13: 230KW power obtained at 53kV using magic 2D

VI. CONCLUSION

Simulation of beam wave interaction for  250 kW CW C-band high power klystron has been done using AJ disk and power obtained at 50 kV in AJ disk is 243 kW and in Magic we obtained power of 230kW at 53 kV and further at 50 kV it is in progress using Magic 2D pic code.

Acknowledgment

We are thankful to the Dr. Chandrasekhar director CEERI PILANI and Dr. S.N Joshi for their encouragement and guidance.

REFERENCES

1.Liao, Samuel Y, Microwave devices and circuits, third    	edition Prentice Hall of India Private Limited.

2. Gilmour, A.S, Microwave Tubes, Artech House, 1986.

3. Kosmahl, H.G. and Albers, L.U., Three dimensional evaluation of energy extraction in output cavities of klystron amplifiers, IEEE Trans. ED-20, pp.883-890, (1973).

4. Kosmahl, H.G. and Branch, G.M. Jr., Generalized representation of electric fields in interaction gaps of klystrons and TWTs, IEEE Trans. ED-20, pp.621-629,(1973).

5. Robert M. Philips and Daryl W. Sprelin, High power       klystrons for next linear colliders, Proceeding of      I EEE, Vol   87, No.5, May 1999.